What to Do When It is
Already Too Late ?
Crashdumps for Embedded Systems
Christoph Sterz christoph.sterz@kdab.com

---
Section slide
❤️ Embrace the Fail

---
Content
- The nature of a crash and where to intercept
- Working with core dumps
- Signal handlers and watchdogs
- My serving suggestion:
  - Yocto, and…
  - Google Breakpad, and…
  - Sentry
- On collecting crashdumps in production

---
Scope of Crashes in this Talk
- Crashes mostly in C/C++
- On Embedded Linux
- Crashes induced from the inside and from the outside
- No Kernelpanics, etc.
- SW-Devs’ Assumption #1: Hardware just works

---
breakpad.bbclass contains this, always executed for a class inheriting breakpad
Crashes in Development And Production
- Dev Environment on Embedded Devices
  - All Symbs / (Remote) GDBs
  - Fullsize dumps
  - EvalBoards
  - Small Testing Surface
- In Production
  - Slim Images
  - Slim Dumps / Reduced Bandwidth
  - (Often more limited) production hardware, no storage
  - Large Testing Surface

---
Programs crash from the inside out
libs / frameworks
& your code
c-runtime
process
systemd, systemv, appmanager, OS
hardware
v
v

---
Quick Setup: Enable Coredumps
Image : Jussi Kilpelainen

---
Prerequisites
- CONFIG_COREDUMP enabled in the Kernel
- Executable must be readable (guess why?)
- Process must have permissions to write the core
- You need enough space to store it
- You need enough Bandwidth to transfer it

---
Enable by setting limits

---
/proc/sys/kernel/core_pattern
Path containing %P %u %g %s %t %c %h
hostname
coresize
PID
uid
gid
signal
time of dump

---
CoreDumps: Did you know?
- You can madvise memorypages to be excluded from Coredump
  - Use madvise with MADV_DONTDUMP flag
- You can pipe coredumps to stdin of another process
  - Make your corePattern start with a | character, followed by the receiving process
  - Systemd coredumpctl does It |/usr/lib/systemd/systemd-coredump
- GDBs gcore can create a core of a running process

---
Development: have GDB on your target!
- At the Development Stage, just have a gdb on the target
- Find a way to store the coredump
- If you get a Crash producing a coredump, rejoin symbols:
  - Use the elfutils bin eu-unstrip <executable> <symbols>
  - Repeat for all relevant libraries you need for heap / stack
- Its a bit tedious, its worth it, if you need heap information
- If no heap is needed, there are better ways

---
You need it all for Cross-Platform CoreDumps 😬
- A cross-toolchain GDB on your Desktop
- The exact same executable that crashed (/w symbols)
- Symbols for all relevant libs when it crashed
- The core file
- Optionally /proc/kallsyms from the target
- Carefully feed SDK-Paths and Libs and see if you get a stack

---
GDB-Server: symbols on the host
App
symbols
Lib
symbols
executable
cross-gdb
gdbserver
host
target

---
Poor-Man’s SlimDump: Backward-Cpp

---
By François-Xavier Bourlet, @bombela
– The Pitch
Tired of seeing this ?

---
Then Try this :)

---
BackwardCpp
- This is in the Development-Situation category
- Include a header + 1 Line of initialization
- Symbols are necessary in build (-g), fat binaries
- Does Stack Unwinding in the signal handlers
- Requires the source code to print it
- Can be heavily customized
  → This is great for Development!

---
The Sanitizers can help you as well.

---
Crash output of an executable, instrumented with the gcc/clang address sanitizer

---
No Symbols? / Unwinding Fails?
Try “Desperate-Stack-Reading”

---
Printing raw stack memory, garnished with symbols
take everything with teaspoons of salt

---
Signal Handlers can act
when its already too late
But they are limited
– use them with care!

---
Linux kill / OOMKiller
🔪
Program
Invalid Memory Access
Signalhandler
Signal proc mask
🎭
OS sends signal

---
Things not allowed in the SignalHandler
- Heap allocations are forbidden from this point on
- One is only permitted to execute “safe” operations
  - That is basically everything that does not allocate
  - Check man signal-safety for it
  - Code looks much like pure C-Code then
- Be hyper-careful of Crashes in Crash Handlers.
  You have been warned :)

---
Things allowed in the SignalHandler
- Start new processes (wow!)
- Obviously reading heap memory
- Again, everything that man signal-safety allows you to do
- Send signal to self

---
Signalhandlers / Crashhandlers look much like plain C Code

---
🕶️ Cool Things possible in the Signal Handler
- Check out the KDABs QML StacktraceDumper.
  - Actually unsafe, because allocates
  - but worth the gamble, its too late anyways, right?
- Start new processes (wow!)

---
Watchdog-like processes can assist

---
It makes sense to have Watchdogs
out of the main execution Context
- There is not only Crashes, but also infinite loops
  - Idea: Reset the watchdog periodically, such that infinite loops are detected
- It can make a lot of sense to inject SIGSEGV & friends from the outside
- A stacktrace will still be produced and Analysis is possible

---
OOMkiller
- Most famous external source of an unwanted termination
- Stackdumps are of limited use in Analysis here
- Sends SIGKILL in rare cases also SIGTERM
  - Catch them and act accordingly (record the memory situation)

---
In Testing and Production:
Breakpad + Sentry on Yocto

---
General Architecture
SymbolServer
Email
Yocto
Sentry
native
Break-
pad
⚡
Crash
Hardware
App
Symbols

---
Integrate Breakpad into Yocto
- Breakpad Recipes included in meta-oe/recipes-devtools
  - Creates all cross-tools needed
  - Creates the header-only library needed for the custom Signal Handler
  - Provides a yocto bbclass to be added to your app recipe
    - This then splits out symbols before app-binary is stripped by yocto

---
breakpad.bbclass contains this, always executed for a class inheriting breakpad
myapp.bb: I extend the breakpad step to have 2 executables and do the upload on every build
… now every yoctobuild uploads the symbols !

---
For the other libs, I use the yocto-built SDK, it contains split debug symbols in .debug folders
Example for file libQt5Core.so : It is important, that debug info is present
… from there it is uploaded like all symbs with sentry-cli

---
More Infos on Breakpad
- Uses Minidumps
  - Originally envisioned by Microsoft
  - Similar to slim cores, but way smaller (around 20KiB)
  - Cross-platform (unix cores don’t work on Windows, settled on minidump)
  - Splitting command: dump_symbs executable > /path/to/destination.symbs
- Minidump comes with some useful tools
  - minidump_stackwalk: Re-Combine Minidump+App+Symbols → get a stack
  - minidump-2-core: Converts App
  - and more…

---
Integrate Breakpad in your Code
- Breakpads library and header are included in the new SDK
  when using it in any recipe.
- Only 2 lines in main are necessary
- Of course you can do more in your custom Handler

---
Include Breakpad Header, (you need to link against libbreakpad_client.a)
Handle crashes and write extra information
Register the Handler in your main, pass any variables to be used

---
Sending the Information
- Decided to let a daemon check /tmp for crashes
  - Not known if device has Connectivity
  - Daemon checks periodically if a minidump is available
  - Based on Settings, Info is uploaded to the Sentry Server
- For now, no logs are “garnished” , maybe in the future

---
Snip from the Crashdaemon,
A file watcher looks for crash data and uploads it, when possible
Extra tag info is garnished for sentry

---
The Result

---
The Result(II)

---
Mail

---
Extra Information on Sentry
- FOSS Dump Collector
- Sorts Crashes by Stack, configurable
- Supports many DumpFormats
- Suppports external Symbol Servers
- ~30€/mo or self hosted

---
GDPR?
<Im not a lawyer>, but… ⚖️

---
On Uploading Crashdata
- We run it for Development / Staging / Testing only
- If Production is involed, make it Opt-In for users
- Practically Stack information can contain all Information
- If Dumps are anonymized and users know for what purpose the data is collected, one should be fine
  … </but Im not a lawyer>

---
Overall there are many ways to learn from your crashes
I showed you one way I like
Invest in learning from your crashes

---
End Of Talk!
I will answer all questions, AMA!